## Slide 1
Phase Noise and Jitter in Oscillator
Aatmesh Shrivastava
Robust Low Power VLSI Group
University of Virginia

## Slide 2
Outline
Phase Noise
  Definition
  Impact
  Q of an RLC circuit
RLC Oscillator
  Phase noise and Q
  Other definition of Q
  Linear oscillatory system
Ring Oscillator
  Transfer curve/power spectral density
  Components of Phase-Noise in a ring oscillator
  Results
Phase Noise and Jitter
  Relation b/w phase noise and jitter
  Inverter jitter due to white Noise
  Ring Oscillator jitter

## Slide 3
Phase Noise : Definition
Reference
B Razavi “A study of Phase Noise in CMOS Oscillator” IEEE Journal of Solid State Circuits Vol.31 3rd March 1996
ωo
ω
Ideal Oscillator
ωo
ω
Actual Oscillator
Δω
  For an ideal oscillator operating at ωo, the spectrum assumes the shape of an impulse
  Actual oscillator exhibits “skirts” around carrier.
  Phase noise at an offset of Δω, is the Power relative to carrier in unit bandwidth

## Slide 4
Phase Noise : Impact
ωo
ω
ωo
ω
Transmit Path
  Interference in both receive and transmit path.
  In RF systems this results in interference.
  In clocks powering microprocessor, the phase noise results in timing issues.
Signal Band
Ideal
LO
Down-converted Band
ωo
ω
Wanted Signal
Actual
LO
Down-converted sign
ω
ω
ω
ω
Unwanted Signal
Receive Path
Nearby Transmitter
Wanted Signal
Effect of Phase Noise
Reference
B Razavi “A study of Phase Noise in CMOS Oscillator” IEEE Journal of Solid State Circuits Vol.31 3rd March 1996

## Slide 5
Quality Factor of an RLC circuit
ωo
Δω
3dB
ωo
Q = ωo/Δω = Lωo/R
  Quality factor Q, of an RLC circuit is the ratio of center frequency and its two sided -3db bandwidth.
  As series resistance increases the Q drops
Reference
B Razavi “A study of Phase Noise in CMOS Oscillator” IEEE Journal of Solid State Circuits Vol.31 3rd March 1996

## Slide 6
Frequency response of RLC Circuit
ωo
Phase noise and Q
  Oscillator shown in the figure. We assume initially, there is only noise at IN.
  The amplifier amplifies all the component of noise frequency by A that are lower than its BW.
  RLC passes component only around ωo, rest are attenuated.
  Voltage at IN is now increased and is at ωo which is again amplified and process repeats till oscillation saturates.
  RLC circuit passes voltages around ωo as well, Higher the Q , lower is the power at other frequencies.
R
L
C
Noise Spectrum
ω
ω
A/(1+jω/ωc)
A
ωc
A
ωo
OUT
IN
ωo
Reference
B Razavi “A study of Phase Noise in CMOS Oscillator” IEEE Journal of Solid State Circuits Vol.31 3rd March 1996

## Slide 7
Other Definition of Q
Not all the oscillator are based on RLC circuit. Ex. Linear Oscillatory system
Q = 2π*(Energy Stored)/Energy dissipated.
Q = ωo/2 dφ/dω
R
L
C
ωo ω
Φ=arg{H(jω)}
H(jω)
+
+
-
X(jω)
Y(jω)
Y(jω)/ X(jω)=H(jω)/(1+H(jω))
It will oscillate at ωo if H(jωo)=-1
However above definition of Q will not apply to this.
Reference
B Razavi “A study of Phase Noise in CMOS Oscillator” IEEE Journal of Solid State Circuits Vol.31 3rd March 1996

## Slide 8
Linear oscillatory system
H(jω)
+
+
-
X(jω)
Y(jω)
Y(jω)/ X(jω)=H(jω)/(1+H(jω))
It will oscillate at ωo if H(jωo)=-1
For phase noise we want to know the power around ωo
For ω=ωo +Δω
H(jω)=H(jωo)+ ΔωdH/dω ……………… using Taylor's series
So,
Y/X= (H(jωo)+ ΔωdH/dω)/(1+ H(jωo)+ ΔωdH/dω)
Y/X= -1/ΔωdH/dω
Reference
B Razavi “A study of Phase Noise in CMOS Oscillator” IEEE Journal of Solid State Circuits Vol.31 3rd March 1996

## Slide 9
Linear oscillatory system
Power spectral density around ωo
|Y/X|2= 1/Δω2|dH/dω|2
H(jω)=A(ω)exp[jφ(ω)]
dH/dω=(dA/d ω+jAdφ/dω)exp(jφ))
At ω=ωo A=1
So,
|Y/X|2= 1/Δω2 {(dA/dω)2 +(dφ/dω)2} …… (i)
gives power in the neighborhood of ωo
Q= ωo/2√ {(dA/dω)2 +(dφ/dω)2}
Reference
B Razavi “A study of Phase Noise in CMOS Oscillator” IEEE Journal of Solid State Circuits Vol.31 3rd March 1996

## Slide 10
Ring Oscillator
C
-Gm
R
C
-Gm
R
C
-Gm
R
Transfer function of each stage is given by H1(jω)=–GmR/(1+jωRC)
Open loop transfer function given by H(jω)={-GmR/(1+jωRC)}3
Using the condition for oscillation we get GmR=2 and ωo=√3/RC
So,
  H(jω)=-8/(1+j√3ω/ωo)3
  Using this we have
  |dA/dω|=9/4ωo |dφ/dω|=3√3/4ωo ……..(ii)
Reference
B Razavi “A study of Phase Noise in CMOS Oscillator” IEEE Journal of Solid State Circuits Vol.31 3rd March 1996

## Slide 11
Additive Noise
C
-Gm
R
C
-Gm
R
C
-Gm
R
  Thermal Noise is additive
  |V1tot[j(ωo+Δω)]|2=R2/9(ωo/Δω)2In2 Where In12 =In22 =In32 =In2
  = 8KTR/9(ωo/Δω)2 Where thermal noiseIn2 =8kT/R
In1
In2
In3
V1
V2
V3
Reference
B Razavi “A study of Phase Noise in CMOS Oscillator” IEEE Journal of Solid State Circuits Vol.31 3rd March 1996

## Slide 12
High Frequency Multiplicative Noise
The Non linearity in the ring oscillator elements, particularly when devices are turning off results in production higher frequency noise.
Vout=a1Vin+a2Vin2+a3Vin3
If Vin= AoCosωot+AnCosωnt
Following noise components are produced
  Cos(ωo+/-ωn)t , Cos(ωo-2ωn)t & Cos(2ωo-ωn)t
Reference
B Razavi “A study of Phase Noise in CMOS Oscillator” IEEE Journal of Solid State Circuits Vol.31 3rd March 1996

## Slide 13
Low Frequency Multiplicative Noise
Noise comes into picture for current source based oscillator
This will result in generation of following component.
Iss+Im
Power in these components is given by
  Cos(ωo+ωn)t , Cos(ωo-ωn)t
  |Vn|2=1/4(KVCO/ωm)2I2m
Reference
B Razavi “A study of Phase Noise in CMOS Oscillator” IEEE Journal of Solid State Circuits Vol.31 3rd March 1996

## Slide 14
Power Noise Trade-off
If we add N oscillators in series, the power will increase by N2.
However, the power in the noise will increase by N as noise will be un-correlated.
So phase noise decreases as power is increased.
  = 8KTR/9(ωo/Δω)2= 4KT/9Gm(ωo/Δω)2
+
ωo
ωo
ωo
ωo
Osc 1
Osc 2
Osc N
Reference
B Razavi “A study of Phase Noise in CMOS Oscillator” IEEE Journal of Solid State Circuits Vol.31 3rd March 1996

## Slide 15
Result
Simulated ring oscillator spectrum with injected white noise.
Reference
B Razavi “A study of Phase Noise in CMOS Oscillator” IEEE Journal of Solid State Circuits Vol.31 3rd March 1996

## Slide 16
Relationship b/w jitter and phase noise
Reference
Asad A. Abidi “Phase Noise and Jitter in CMOS ring oscillators” IEEE Journal of Solid State Circuits Vol.41 3rd August 2006
…. (i) using Weiner-khinchine theorum

## Slide 17
Relationship b/w jitter and phase noise
Reference
Asad A. Abidi “Phase Noise and Jitter in CMOS ring oscillators” IEEE Journal of Solid State Circuits Vol.41 3rd August 2006
fo
Phase Noise PSD because of white Noise is given by
Now we can use this to evaluate (i)

## Slide 18
Inverter Jitter due to white Noise
Reference
Asad A. Abidi “Phase Noise and Jitter in CMOS ring oscillators” IEEE Journal of Solid State Circuits Vol.41 3rd August 2006
White Noise because of the NMOS discharge current is given by
… (ii) From 4KT/R
If the inverter trips at VDD/2 then correct discharge equation would be

## Slide 19
Inverter Jitter due to white Noise
Reference
Asad A. Abidi “Phase Noise and Jitter in CMOS ring oscillators” IEEE Journal of Solid State Circuits Vol.41 3rd August 2006
Where tdN is a random variable and its statistics follows
Mean
Mean-sqaure

## Slide 20
Inverter Jitter due to white Noise
Reference
Asad A. Abidi “Phase Noise and Jitter in CMOS ring oscillators” IEEE Journal of Solid State Circuits Vol.41 3rd August 2006
Now we can think tdN as a rectangular time window
So its frequency response will have sinc function
Spectral density tdN
using Weiner-khinchine theorum
using (ii) Noise spectral density of discharge current

## Slide 21
Inverter Jitter due to white Noise
Reference
Asad A. Abidi “Phase Noise and Jitter in CMOS ring oscillators” IEEE Journal of Solid State Circuits Vol.41 3rd August 2006
Now we can think tdN as a rectangular time window
So its frequency response will have sinc function
Spectral density tdN
using Weiner-khinchine theorum
using (ii) Noise spectral density of discharge current

## Slide 22
Inverter Jitter due to white Noise
Reference
Asad A. Abidi “Phase Noise and Jitter in CMOS ring oscillators” IEEE Journal of Solid State Circuits Vol.41 3rd August 2006
Prior to switching even the pull-up transistor (PMOS) deposits initial noise on cap.
Total Jitter therefore is given by

## Slide 23
Ring Oscillator Jitter and Phase Noise
Reference
Asad A. Abidi “Phase Noise and Jitter in CMOS ring oscillators” IEEE Journal of Solid State Circuits Vol.41 3rd August 2006
In a ring oscillator if there are M stages, there would be M rise transition and M fall transition.
So oscillation frequency is given by
Every rise of fall event will add in mean square as they would be un-correlated
Using jitter from each rise and fall transition

## Slide 24
Ring Oscillator Jitter and Phase Noise
Reference
Asad A. Abidi “Phase Noise and Jitter in CMOS ring oscillators” IEEE Journal of Solid State Circuits Vol.41 3rd August 2006
One obtains phase Noise in ring oscillator
Conclusions
Phase Noise does not depend on number of stages in ring oscillator. ( same for heavily loaded few stage or many stages lightly loaded.
Phase noise lower for higher VDD.
Lower phase noise for Lower Vt.
Increase current to reduce phase noise.

## Slide 25
Ring Oscillator or LC oscillator
Reference
Asad A. Abidi “Phase Noise and Jitter in CMOS ring oscillators” IEEE Journal of Solid State Circuits Vol.41 3rd August 2006
For the same noise performance a ring oscillator would need 450 times more current compared to an LC oscillator.